## Slide 1: FOCES: Detecting Forwarding Anomalies in Software Defined Networks
Peng Zhang1, Shimin Xu1, Zuoru Yang1, Hao Li1 , Qi Li2 , Huanzhao Wang1 , Chengchen Hu1
1Xi’an Jiaotong University 2Tsinghua University
ICDCS 2018
Notes: Good morning everyone, my name is Zuoru Yang.
It is my honor to represent our group to present our research work, call FOCES,
which can be used to detect the forwarding anomaly in SDN

## Slide 2: Introduction
Forwarding abstraction of Software Defined Network (SDN)
  Match-Action model
A packet:
  1. match a rule in switches
  2. execute the related actions
  3. update the counter
 | Match | Action | Counter
Rule 1 | dst_ip=10.0.0.0/8 | forward to port 2 | 3
Rule 2 | dst_ip=192.168.0.0/16 | forward to port 3 | 2
… | … | … | 
2
3
1
dst_ip=10.0.0.1
dst_ip=192.168.1.1
S1
S1’s forwarding table
S0
S2
S3
Notes: As we know, the forwarding process of SDN can be abstracted as a Match-Action Model.
In detail, all flows rules are stored in the Flow Table.
When a packet arrives at a switch, it would first match a rule in flow table.
And execute related actions, then update the corresponding counter of it.
Here is a simple example to show the forwarding process in SDN

## Slide 3: Forwarding Anomaly
Normally, Forwarding anomaly can be classified into three types:
  Early Drop: S1->⊥
  Switch Bypass: S1->S5, S1->S3->S4->S5
  Detour: S1->S2->S3->S4->S2->S5
S1
S2
S3
S5
S4
S0
Forwarding anomaly can cause violation of critical security policy
  Flow may bypass the firewall
  ….
Notes: A recent study shows that the attacker can tamper the forwarding path of some flows
  By Hack the operating systems of SDN switches
  Attack the control channels
If a flow does not traverse along its original path, then we say it is forwarding anomaly.
Generally, forwarding anomaly can be classified into three types:
As can be seen from this example, the original path of the flow in green is switch S0 S1 S2 and S5
Suppose here an attacker has controlled S1
For Early Drop, it means packets are dropped before reaching the destination switch.
And Switch Bypass is packets are received by the destination switch, but one or more switch are skipped
Path Detour is a little complex, it means packets deviate from one switch and com back to this switch later.
When forwarding anomaly happens, it may break the critical security policy.
For example, …. Which can introduce the issue of security.

## Slide 4: Countermeasures
Rule Dumping
  Read all the forwarding rules from suspicious switches, and checks the integrity of them
  Limitation: compromised switches can easily bypass the detection by just reporting the original rules
Path Validation
  Each switch imprints packets with signature, so that the destination switch can check whether the path traversed by a packet is correct.
  Limitation: need to modify switches to support cryptographic operations, high overhead.
Notes: To detect the forwarding anomaly, here are two simple methods.
However, both of them have some limitations.
The most intuitive one is dumping rules from suspicious switch, and check their integrity.
However, the compromised switch can bypass this detection easily.
A little more reliable way is to let each switch imprints packets with signature.
Thus, the egress switch can check whether path is correct.
But this kind of method needs to modify the switch, and the overhead of it is always very high.

## Slide 5: Intuition of Statistics Verification
Packets leave traces (i.e., counters) when they are forwarded along their paths
If we know how packets SHOULD be forwarded, then we can have constraints on counters of different switches
If the packets deviate from their paths, then the constraints shall be violated.
Notes: Besides those two methods, statistics verification is another prevalent method.
The main idea of this kind of method is packets would leave some evidences in their paths, such as the rule’s counter
Therefore, there should be some constraints of the right forwarding path.
The detection standard is if the packets deviate from their paths, then the constraints shall be violated.

## Slide 6: Toy Example
We know the path should be:
r0, r1, r2, r5 should have the same counter value, and r3, r4 should have zero counter value. (“Flow Conservation Principle”)
S0
S1
S2
S5
r0
r1
r2
r5
S1
S2
S3
S5
S4
S0
r0.counter=a
r3.counter=a
r4.counter=a
r2.counter=0
r1.counter=a
r5.counter=a
r2.counter=a
r3.counter=0
r4.counter=0
a
Notes: Here is an example,
We know the path of a flow should be S0 S1 S2 S5
So the corresponding flow rules should have the same counter value.
We also call this flow conservation principle.
If the attacker has controlled the switch S1 and this flow deviates to another path,
then the counter of rule2 would not be a,
Which breaks the constrains of flow conservation principle.
So it is very easy to detect the forwarding anomaly,
when applying the flow conservation principle to a individual flow

## Slide 7: Toy Example
In real network, there are more than one flows, and each rule may match multiple flows.
e.g., each counter may aggregate multiple flows(wildcard)
S1
S2
S3
S5
S4
S0
r0.counter=a
r3.counter=a
r4.counter=a+c
r2.counter=b
r1.counter=a
r5.counter=a+b+c
a
b
c
Notes: However, in the real network, a flow rule may match more than one flows.
So the distribution of counters can more complex.
And make It hard to apply the flow conservation principle of a individual flow directly.
It needs to install dedicated rules to collect the counter of a given flow.

## Slide 8: The motivation of this work
All the previous statistics verification tools check whether the counters of a individual flow conform to the flow conservation principle.
An Open Question: Can we extend the flow conservation principle from individual flows to a network of flows?
However, applying the flow conservation principle for each individual flow has two serious limitations:
  Limited Detection Scope: miss some forwarding anomalies happening to flows that are not check.
  High Flow Table Overhead: install dedicated rules to collect the statistics of a specific flow.
Notes: So the motivation of our work is:
all the previous statistics verification tools just check whether the counters of a individual flow conform to the flow conservation principle.
However, they have two serious limitations.
First, applying the flow conservation principle to a flow may result in a limited detection scope.
Because it can’t check all the flow simultaneously.
Second, to collect the counter of a individual flow,
it always needs to install dedicated flow rules which introduces high flow table overhead.
As a result, we pose a question.
That is can we extend the flow conservation principle from individual flows to a network of flows

## Slide 9: Outline
Overview
FOCES: Theoretical Construction
FOCES: Make it work
Implementation & Evaluation
Notes: Next, I will illustrate the Theoretical Construction of FOCES

## Slide 10: FOCES: FlOw Counter Equation System
All the flows in the network:
All the rules in the network:
Define the Flow Counter Matrix (FCM) as:
Let the counter of rule be , and
Let the volume of flow be , and
If there are no forwarding anomalies:
Notes: Formally, we define the Flow Counter Equation System as follows.
Suppose there are n flows f1 to fn and m flow rules r1 to rm
We define the Flow Counter Matrix to describe the relationship between flows and rules.
In detail, when flow j matches rule i, then H(i,j)’s value should be 1, otherwise it is 0.
We also define the counter vector and flow volume vector as follows
And the flow volume means the number of packets in this flow
So if there do not exist forwarding anomaly, then we have H timex X will equal to Y

## Slide 11: FOCES: FlOw Counter Equation System
When there are forwarding anomalies, the real FCM will be , and the real counter vector will be .
However, we do not know either or , but it is expected that
should probably has no solutions if , when it is a over-determined equation system
The least square solution will be
and we should have (the standard to judge the anomaly)
Notes: When there are forwarding anomalies, which mean FCM is not the original one, denote it as H prime
So the real counter vector Y prime will be H prime times X.
Generally ,we do not know H prime and flow volume X.
But it is expected that H times X bar equal to Y prime. So we need to solve this equation to get the expected flow volume X bar.
We regard the least square solution X bar as the solution of this equation.
So the expected counter vector will equal to H times X bar.
We use delta to indicate the difference between the expected counter vector and the real counter vector.
It is obvious that delta would not be 0 when there are forwarding anomalies.
So we use it as the standard to judge the anomaly.

## Slide 12: For Example
Forwarding Anomaly
Notes: For example, we suppose an attacker has controlled S1 here.
And modify the rule r1 to forward the flow in green to switch S3
So the FCM has been modify to this form
and the corresponding counters also have changed.
However, we do not realize this modification, we just know the original FCM and the observed counter.
Therefore, we firstly construct this equation system and solve the flow volume vector by using least square solution.
Suppose, the volume of these three flow are 3, 4, 5 respectively.
Then, the least-square solution of this equation system are 3, 1 and 8.
And we find delta is not zero, which means there exists forwarding anomaly.

## Slide 13: Does this method always work?
Unfortunately, No
Notes: It is obvious that this method is not too complex.
However, we also concern another question that is does this method always work?
Unfortunately, No

## Slide 14: For Example
Normal (Wrong Result)
Notes: Let’s review the previous example again, in this time the we let the flow in orange start to traverse from S3,
So original FCM has a little different from last one. And I mark it with the red line.
we do this calculation again,
And get the same least square solution.
However, in this time, delta is zero, which means this network is normal.
So FOCES generates a wrong result.

## Slide 15: The Reason of this Failure
S1
S2
S3
S5
S4
S0
r0.counter=3
r3.counter=8
r4.counter=8
r2.counter=4
r1.counter=3
r5.counter=12
3
4
5
The observed counters in this example
Notes: We want to figure out the reason of this failure,
so we analyze this example in detail.
This shows the observed counter distribution with the true flow volume

## Slide 16: The Reason of this Failure
S1
S2
S3
S5
S4
S0
r0.counter=3
r3.counter=8
r4.counter=8
r2.counter=4
r1.counter=3
r5.counter=12
3
1
8
The estimated counters in this example
  same as the observed one
Finding:
  FOCES cannot work for this case
Question: How to identify the detectability of a given case?
Notes: This show the counter distribution with the least-square solution.
We find counter distribution of it is same as the observed one,
which means the least-square solution may not violate counter constrains because of the feature of flows.
This is the reason why FOCES generates a wrong result this time.
So we further pose a question.
That is how to identify the detectability of a given case?

## Slide 17: Analysis on Detectability
Theorem 1: If is undetectable if and only if lies in the linear subspace generated by
  Theorem 1 is different to apply in real network
  Its algorithm is complex
Theorem 2: If is undetectable if and only if there is a switch whose RBG contains a loop
  reduce Theorem 1 to the problem of finding loops in a bipartite graph
Notes: We analyze the detectability from theoretical perspective.
And the prove this theorem that……….
However, we find this theorem 1 is hard to apply, because its algorithm is complex
To make it more easy and practical to apply,
We pose theorem 2
We introduce the rule bipartite graph for each switch in order to describe the relationship of flows and rule in a fine-grained view
Theorem 2 reduce this theorem 1 to the problem of finding loops in a bipartite graph.

## Slide 18: Review the Failure Example
The Rule Bipartite Graph (RBG) of S2
  a loop marked in green dashed lines
Notes: In order to explain our theorem clearly,
Here show the RBG of switch S2,
The green dashed lines is a loop in it.
which means the least-square solution may not break counter constraints.
For the detail of RBG, please refer our paper.

## Slide 19: Outline
Overview
FOCES: Theoretical Construction
FOCES: Make it work
Implementation & Evaluation
Notes: Then, I will demonstrate how to make FOCES work in real network

## Slide 20: Make FOCES Work in Realistic Settings
Noises:
  Packet losses
  Out-of-sync counter
Scalability:
  Calculating the inverse of FCM is expensive when there are a large number of rules and flows
Hard to apply in large scale network
Notes: To make FOCES work in realistic settings,
There are two challenges to be solved.
First, the packet losses and out of synchronize counter would also lead delta to not be zero in the normal case.
We regard those two factors as noises in the network.
Second, in a larger network, the scale of Flow Counter Matrix would be very large,
Which can cause a high overhead of calculation.

## Slide 21: Threshold-based Detection Algorithm
Basic Idea: define the anomaly index (AI) to measure the possibility of forwarding anomaly, and eliminate the impact of such noises
Anomaly Index:
  the ratio of Maximum and Median of all elements in
  When there are forwarding anomalies, the AI should be very large (“majority good” assumption)
Detection Threshold:
  : forwarding anomalies
  is the default detection threshold (“three-sigma rule” in probability theory)
Notes: To erase the impact of such noises.
We design a threshold-based detection algorithm.
The basic idea of it is to introduce a anomaly index to measure the possibility of forwarding anomaly.
The anomaly index is defined as the ration of Maximum and Median of all elements in delta.
With the majority good assumption, when AI should be very large.
Then we introduce a threshold T, when AI is larger than T,
We suppose there are forwarding anomalies.
We also analyze the default value of this threshold by “three-sigma rule” of probability theory

## Slide 22: Making FOCES Scalable
Basic Idea: make FOCES scalable by reducing the computation time
  It is inspired by the Rule Bipartite Graph (RBG)
  Shrank the scale of FCM
FCM Slicing:
  extract the sub-FCM corresponding to the RBG.
  Sub-FCMs are much smaller than the original FCM, it reduces the computation time.
For Example:
Notes: To make FOCES scalable,
Our idea is to reduce the computation time by sharking the scale of FCM.
This idea is inspired by the RBG.
We observe the RBG for a specific switch only contains a small number of rules rule,
So we extract a sub-FCM corresponding to the RBG.
As can be seen from this example,
The Sub-FCM of switch S2 is much smaller than the original one.
Therefore it can reduce the computation time.

## Slide 23: Making FOCES Scalable
Theorem 3: If a forwarding anomaly is detectable (without slicing), then it is still detectable when using slicing.
  using slicing is equivalent to the baseline method in detecting forwarding anomalies
Analysis on Computation Complexity Reduction:
  without slicing: N is the size of the FCM (approximately equals to that of Matrix Inversion)
  with slicing:
Notes: However, we also concern the equivalence between using slicing and the baseline.
So we pose and prove the theorem that a forwarding anomaly is detectable without slicing,
Then it is still detectable when using slicing.
Finally, we to further investigate the computation complexity of using slicing
According to our analysis, using sling can truly reduce the Computation Complexity from N cubed, to the N to the power 2.3

## Slide 24: Outline
Overview
FOCES: Theoretical Construction
FOCES: Make it work
Implementation & Evaluation
Notes: Next part is about the implementation and evaluation

## Slide 25: Implementation
FOCES prototype:
  1500 LOC in Python
  FCM Generator: ATPG, Floodlight REST API
  Statistics Collector: Floodlight REST API, parse counters
  Equation System Solver: “NumPy” library, “sparse” library of python
Notes: Here, I elaborate how we implement the prototype of FOCES.
the prototype is about 1 thousand and 5 hundred lines of python code
For FCM generator, it uses ATPG and Floodlight REST API to get the matching relationship between flows and rules ,
Then it can construct the Flow Counter Matrix
Statistics Collector also uses Floodlight REST API to get each rule’s counter periodically.
When Equation System Solver gets FCM and counter vector,
It starts to solve the least-square solution.
it achieves matrix inversion and transpose by using NumPy and Sparse Python libraries

## Slide 26: Experiment Setup
SDN Controller: Floodlight v2.1
Network: Mininet + Open vSwitches
Topologies: Stanford, FatTree(4), BCube(1, 4), DCell(1, 4)
Notes: Now, I’ll introduce our experiments
We use Floodlight as the SDN Controller
The network topology is simulated by Mininet and OVS
We generate four network topologies to test FOCES,
And this table here shows the key parameters of those four topologies.
We use Iperf to generate a flow between each pair of hosts.

## Slide 27: Functional Test
Setting
  BCube(1, 4)
  Packet Loss Rates: 0%, 5%, 10%
  Modify a rule: 60s-120s
Finding
  AI quickly goes beyond the threshold, when forwarding anomalies happen.
  Normal and anomaly cases become less distinguishable when packet loss rates increase
Notes: In Functional Test, we test whether FOCES can detect forwarding anomalies.
We randomly modify a rule during 60s to 120s to simulate the attacker.
  And FOCES runs a detection process every 5 second.
This figure shows that anomaly index goes up dramatically when forwarding anomalies happen
However, with the increase of packet loss rate,
The indices for normal and anomaly cases become less distinguishable.
So this experiment shows FOCES can effectively detect forwarding anomalies

## Slide 28: Detection Precision vs. Number of Anomalies
Detection Precision
  Randomly modify 1, 2, and 3 rules.
  Detection threshold: 3.5
Findings
  Precision increases when more rules are modified.
  Packet loss rate 10%: precision 90%
Notes: As for the detection precision, for each packet loss rate.
We randomly modify different number of rules and fix the detection threshold in 3.5.
And each data point is an average of 50 experiment runs.
We find the for a fixed packet loss rate,
precision increases when more rules are modified.
And precision is higher than 90% when packet loss rate is less then 10%.

## Slide 29: Detection Accuracy vs. Detection Threshold
The Recover Operating Characteristic (ROC) Curve
  Detection threshold: 1 ~ 100
  Packet loss rates: 0% ~ 25%
Findings
  Accuracy of FOCES is little affected: Packet Loss Rate 10%
  Best detection threshold: around 4.5
  Best performance: TP rate nearly 100% and a FP rate around 4.3%.
Notes: For detection accuracy, we use ROC curve to indicate accuracies in different thresholds
We vary the detection threshold from 1 to 100 and
Do the experiments with packet loss rates from 0% to 25%.
The figures show the accuracy is little affected when the packet loss rate is below 10%
And the best detection threshold is about 4.5, where the TP rate is nearly 100% and FP rate is just 4.3%.
As a result, this experiment demonstrates FOCES can work well under different condition.

## Slide 30: The Effectiveness of Slicing
Detection Accuracy
  Slicing can achieve an even better detection accuracy, except for BCube(1, 4) topology.
Computation time:
  Topology: FatTree(8)
  Computation time: slicing grows much slower than without slicing.
  Reduction of computation overhead: nearly 80%
Notes: For the effectiveness of slicing, we compare the performance of using slicing and baseline method.
we firstly compare the detection accuracy of them.
We find slicing can achieve an even better accuracy in three topologies.
For computation time
We do this experiment in FatTree.
The figure indicates the computation time of slicing grows much slower than without slicing.
And slicing can reduce the time overhead by 80% when there 12K flows in the network.
In summary, those two experiments show that using slicing can help FOCES achieve a faster detection without loss of detection accuracy

## Slide 31: Conclusions
Study how to extend flow conservation principle from individual flows to a network of flows and how to use it detect forwarding anomalies
Design and analyze FOCES from both theoretical and practical perspectives
Build FOCES prototype and conduct extensive experiments on Mininet with four topologies
  Empirical results match theories
Future Work:
  The localization of the compromised switch (we have just finished it)
Notes: As a result, in this paper, we study……..
Then we design a flow counter equation system, call FOCES, and analyze it from both theoretical and practical perspectives.
Next, we build FOCES prototype and conduct extensive experiments on Mininet with four topologies.
The empirical results match theories.
And the future work is